## Slide 1: Brief on AMD MIVisionX
Alan Zhang

## Slide 2: Overview
MIVisionX toolkit is a set of comprehensive computer vision and machine intelligence libraries, utilities, and applications bundled into a single toolkit. AMD MIVisionX delivers highly optimized open source implementation of the Khronos OpenVX™ and OpenVX™ Extensions along with Convolution Neural Net Model Compiler & Optimizer supporting ONNX, and Khronos NNEF™ exchange formats.
MIVisoinX toolkit components:
  AMD OpenVX & OpenVX Extensions
  Neural Net Model Compiler & Optimizer
  Toolkit
  Utilities

## Slide 3: AMD OpenVX & OpenVX Extensions
  AMD OpenVX Core Lib
  vx_loomsl: Radeon LOOM stitching library for live 360 degree video applications
  vx_nn: OpenVX neural network module that was built on top of MIOpen (i.e. AMD's cuDNN)
  vx_opencv: OpenVX module that implemented a mechanism to access OpenCV functionality as OpenVX kernels
  vx_winml: OpenVX module that implemented a mechanism to access Windows Machine Learning(WinML) functionality as OpenVX kernels
  Runtime OS: Windows w/ OpenCL SDK, Linux w/ ROCm
  Hardware Configuration: CPU: SSE4.1 or above CPU, 64-bit; GPU: Radeon Professional Graphics Cards or Vega Family of Products (16GB required for vx_loomsl and vx_nn libraries)
Notes: Radeon Loom使用AMDKhronos™OpenVX™开源计算视觉架构，可实时拼接多至24个4k x2k镜头、离线拼接多至31个8K x4K镜头拍摄到的画面。

## Slide 4: Applications Based on AMD OpenVX
Cloud Inference Application: This sample application does inference using a client-server system.
Digit Test: This sample application is used to recognize hand written digits.
MIVisionX OpenVX Classsification: This sample application shows how to run supported pre-trained caffe models with MIVisionX RunTime.
MIVisionX WinML Classification: This sample application shows how to run supported ONNX models with MIVisionX RunTime on Windows.
MIVisionX WinML YoloV2: This sample application shows how to run tiny yolov2(20 classes) with MIVisionX RunTime on Windows.
External Applications
Notes: https://gpuopen-professionalcompute-libraries.github.io/MIVisionX/apps/mivisionx_openvx_classifier/
https://github.com/srohit0/trafficVision#traffic-vision

## Slide 5: AMD OpenVX Client/Server Demo App

## Slide 6: Neural Net Model Compiler & Optimizer
Neural Net Model Compiler & Optimizer converts pre-trained neural network models to MIVisionX runtime code for optimized inference.
MIVisionX RunTime: AMD OpenVX + OpenCV-Interop Kernels
Pre-requisites: Install ROCm, and MIVisionX, numpy, onnx, nnef-parser
Model Compiler & Optimizer Usage
  Step 1 - Convert Pre-trained model to AMD NNIR, pre-trained models can be Caffe, ONNX, NNEF;
  Step 2 - Apply Optimizations
    Update batch size in AMD NNIR model
    Fuse operations in AMD NNIR model
    Quantize the model to float 16
    Workaround groups using slice and concat operations in AMD NNIR model
  Step 3 - Convert AMD NNIR to OpenVX C code w/ nnir_to_openvx.py
Notes: Models & Operators currently supported:
https://gpuopen-professionalcompute-libraries.github.io/MIVisionX/model_compiler/#mivisionx-runtime

## Slide 7: MIVisionX Toolkit
AMD MIVisionX Toolkit, is a comprehensive set of help tools for neural net creation, development, training and deployment.
Output result
  Overall Summary
  Graphsgraph
  Labels
  Image Results
  Compare
  Model Score

## Slide 8: Utilities
inference_generator: generate inference library from pre-trained CAFFE models
  caffe2openvx: Convert a pre-trained CAFFE model into a C library for use by applications.
loom_shell: an interpreter to prototype 360 degree video stitching applications using a script.It provides direct access to Live Stitch API by encapsulating the calls to enable rapid prototyping.
RunVX: command-line utility to execute OpenVX graph described in GDF text file
RunCL: command-line utility to build, execute, and debug OpenCL programs

## Slide 9: Backup

## Slide 10: ROCm - AMD Openning Software Stack for GPU Programming
Notes: http://developer.amd.com/wordpress/media/2013/06/2620_final.pdf

## Slide 11: AMD ROCm 2.6 Software Stack
ROCm Core Components
  ROCk Kernel Driver
  ROCr Runtime
  ROCt Thunk Interface
ROCm Support Software
  ROCm SMI
  ROCm cmake
  rocminfo
  ROCm Bandwidth Test
ROCm Development Tools
  HCC compiler (Like NVCC)
  HIP (Like CUDA)
  ROCm Device Libraries
  ROCm OpenCL Runtime, Driver, Compiler
  ROCM Clang-OCL Kernel Compiler
  Asynchronous Task and Memory Interface (ATMI)
  ROCr Debug Agent
  ROCm Code Object Manager
  ROC Profiler
  ROC Tracer
  Radeon Compute Profiler
ROCm Libraries
  rocBLAS/Tensible w/ BFloat16 support
  hipBLAS w/ rocBLAS and cuBLAS as backend
  rocFFT
  rocRAND
  rocSPARSE
  hipSPARSE
  rocALUTION
  MIOpenGEMM
  MIOpen 2.0 w/ BFloat16 support (Like cuDNN)
  rocThrust
  MIGraphX 0.3
  ROCm SMI Lib
  RCCL
  MIVisionX
  hipCUB
Notes: Reference:
https://github.com/RadeonOpenCompute/ROCm
The ROCr System Runtime is language independent and makes heavy use of the Heterogeneous System Architecture (HSA) Runtime API.
HSA defines a unified virtual address space for compute devices.
the HSA specifications cover:
HSA Intermediate Layer: HSA Intermediate Layer (HSAIL), a virtual instruction set for parallel programs.
HSA memory model
HSA dispatcher and run-time: ROCr API is essentially the HSA Runtime API plus extensions for discrete GPUs and peer-to-peer communication.
HSA Runtime API
Define a set of hardware requirements
rocALUTION can be seen as middle-ware between different parallel backends and application specific packages.
Various backends supported by rocALUTION:
Host - fallback backend, designed for CPUs
GPU/HIP - accelerator backend, designed for HIP capable AMD GPUs
OpenMP - designed for multi-core CPUs
MPI - designed for multi-node and multi-GPU configurations
MIOpenGEMM: A tool for generating OpenCL matrix multiplication (GEMM) kernels.
ROCm 2.7 will bring in Navi support.
About BFloat16:
Software support for BFloat16 on Radeon Instinct MI50, MI60 has been added. This includes:
Mixed precision GEMM with BFloat16 input and output matrices, and all arithmetic in IEEE32 bit
Input matrix values are converted from BFloat16 to IEEE32 bit, all arithmetic and accumulation is IEEE32 bit.Output values are rounded from IEEE32 bit to BFloat16
Accuracy should be correct to 0.5 ULP

## Slide 12: Layer Model of ROCm Stack & Language
Three Level Compilation Foundation & Language Support
  LLVM compiler foundation
  HCC C++ and HIP for application portability
  GCN assembler and disassembler
Notes: Reference:
GCN Native ISA LLVM Code Generator:
https://rocm-documentation.readthedocs.io/en/latest/ROCm_Compiler_SDK/ROCm-Native-ISA.html
http://llvm.org/docs/AMDGPUUsage.html
Note: The AMDGPU backend provides ISA code generation for AMD GPUs, starting with the R600 family up until the current GCN families. It lives in the lib/Target/AMDGPU directory.

## Slide 13: AMD AI over ROCm
Framework | Status | MIOpen Enabled | Upstreamed | Current Repository
Caffe | Public | Yes |  | https://github.com/ROCmSoftwarePlatform/hipCaffe
Tensorflow 2.0 | Verified | Yes | CLA in Progress | Notes: Working on NCCL and XLA enablement, Running
Caffe2 | Upstreaming | Yes | CLA in Progress | https://github.com/ROCmSoftwarePlatform/caffe2
Torch HIP | Upstreaming | Development | In process | https://github.com/ROCmSoftwarePlatform/cutorch_hip
HIPnn | Upstreaming | Development |  | https://github.com/ROCmSoftwarePlatform/cunn_hip
PyTorch | Development | Development |  | 
MxNet | Development | Development |  | https://github.com/ROCmSoftwarePlatform/mxnet
CNTK | Development | Development |  | 
Notes: Tensorflow ROCm port This project is based on TensorFlow 1.14.0. It has been verified to work with the latest ROCm2.6 release. Please follow the instructions here to set up your ROCm stack. A docker container: rocm/tensorflow:latest(https://hub.docker.com/r/rocm/tensorflow/) is readily available to be used.

## Slide 14: Application Development over ROCm Stack
Languages support
  HCC: C++ dialect with extensions to express all forms of parallelism, including multicore CPU, SIMD and GPU.
  HIP: C++ dialect designed to ease conversion of Cuda applications to portable C++ code.It provides a C-style API and a C++ kernel language.
  OpenCL: provides a C run-time API and C99-based kernel language.
  Python w/ Numba: Support acceleration of HSA APUs, as well as ROCm-enabled discrete GPUs via Numba that can convert array-oriented and math-heavy Python code to native machine instructions.It supports Python compilation to run on either CPU or GPU hardware and is designed to integrate with Python scientific software stacks, such as NumPy.
GCN Version | GPU/APU Family | Example of Radeon GPU
gfx701 | GFX7 | FirePro W8100, FirePro W9100, Radeon R9 290, Radeon R9 390
gfx801 | Carrizo APU | FX-8800P
gfx803 | GFX8 | R9 Fury, R9 Fury X, R9 Nano, FirePro S9300 x2, Radeon RX 480, Radeon RX 470, Radeon RX 460
gfx900 | GFX9 | Vega10
Notes: HCC: An open source C++ compiler for heterogeneous devices, that takes a application program that confroms to a parallel programming standards such as C++ AMP, HC, C++ 17 ParallelSTL, or OpenMP, and transforms it into the AMD GCN ISA. The project is based on LLVM+CLANG. https://github.com/RadeonOpenCompute/hcc/wiki
Reference:
https://gpuopen.com/rocm-do-you-speaka-my-language/

## Slide 15: AMD Graphics Core Next
GCN is a RISC SIMD (or rather SIMT) microarchitecture, it has been developed GCN 5th ISA, and Vega ISA.
Highlight GCN 5th Design
  Increase instructions per clock, higher clock speeds, support for HBM2, a larger memory address space
  Discrete GFX chipsets integrates "HBCC (High Bandwidth Cache Controller)", not in APU
  Stream processors support packed math Rapid Pack Math technology for 8-bit, 16-bit, and 32-bit numbers
  All GCN 5th generation GPUs support half-precision floating-point (FP16) calculations which is double of FP32 performance.
  Primitive Shaders
Notes: "Graphics Core Next" shall refer to the entire GPU; hence it is possible that the same version of the GCA (the 3D engine) is combined with different versions of the DIF.
GCN graphics chips are fabricated with CMOS at 28 nm, and with FinFET at 14 nm (by Samsung Electronics and GlobalFoundries) and 7 nm (by TSMC), available on selected models in the Radeon HD 7000, HD 8000, 200, 300, 400, 500 and Vega series of AMD Radeon graphics cards, including the separately released Radeon VII. GCN is also used in the graphics portion of AMD Accelerated Processing Units (APU), such as in the PlayStation 4 and Xbox One APUs.
Chips
discrete GPUs:
Vega 10 (14 nm Samsung/GloFo FinFET process) (also codenamed Greenland[46]) found on "Radeon RX Vega 64", "Radeon RX Vega 56", "Radeon Vega Frontier Edition" and "Radeon Pro V340" graphics cards[47]
Vega 12 (14 nm Samsung/GloFo FinFET process) found on "Radeon Vega Pro 20" and "Radeon Vega Pro 16"-branded mobile graphics cards[48]
Vega 20 (7 nm TSMC FinFET process) found on "Radeon Instinct MI50" and "Radeon Instinct MI60"-branded accelerator cards[49] and "Radeon VII"-branded graphics cards[50].
integrated into APUs:
Raven Ridge[51] came with VCN 1 which supersedes VCE and UVD and allows full fixed-function VP9 decode.

## Slide 16: Vega Series Processor
The DPP array is the heart of the GCN processor. The array is organized as a set of compute unit (CU) pipelines operating in parallel on streams of floating-point or integer data.
GCN processor groups 64 work-items into a wavefront, which executes the kernel on all 64 work-items in one pass.
The GCN processor consists of:
  A scalar ALU, which operates on one value per wavefront (common to all work items).
  A vector ALU, which operates on unique values per work-item.
  Local data storage, which allows work-items within a workgroup to communicate and share data.
  Scalar memory, which can transfer data between SGPRs and memory through a cache.
  Vector memory, which can transfer data between VGPRs and memory,including sampling texture maps.
Notes: Reference:
Vega ISA: https://rocm-documentation.readthedocs.io/en/latest/GCN_ISA_Manuals/testdocbook.html#testdocbook
The GCN device includes a data-parallel processor (DPP) array, a command processor, a memory controller, and other logic (not shown). The GCN command processor reads commands that the host has written to memory-mapped GCN registers in the system-memory address space. The command processor sends hardware-generated interrupts to the host when the command is completed.
Workgroup: A workgroup is a collection of wavefronts that have the ability to synchronize with each other quickly; they also can share data through the Local Data Share.
Wavefront: A collection of 64 work-items that execute in parallel on a single GCN processor.
Work-item: A single element of work: one element from the dispatch grid, or in graphics a pixel or vertex.

## Slide 17: Compute Unit (CU) and Memory Hierarchy
Local Data Share (LDS)
  This memory is configured with 32 banks, each with 512 entries of 4 bytes that enables low-latency communication between work-items within a work-group, or the work-items within a wavefront
Global Data Share (GDS)
  GDS is configured with 32 banks, each with 512 entries of 4 bytes each.

## Slide 18: Backup

## Slide 19: AMD ROCm Overview
ROCm之于AMD GPU，基本上相当于CUDA 之于NVIDIA GPU。
ROCm的目标是建立可替代 CUDA 的生态，并在源码级别上对 CUDA 程序的支持。为了实现目标，ROCm 复制了 CUDA 的技术栈。
Notes: https://blog.csdn.net/JackyTintin/article/details/74637157
ROCm Software Platform:
https://github.com/ROCmSoftwarePlatform

## Slide 20: ROCm vs CUDA
CUDA | ROCm | 备注
CUDA API | HIP | C++ 扩展语法
NVCC | HCC | 编译器
CUDA 函数库 | ROC 库、HC 库 | 
Thrust | Parallel STL | HCC 原生支持
Profiler | ROCm Profiler | 
CUDA-GDB | ROCm-GDB | 
nvidia-smi | rocm-smi | 
DirectGPU RDMA | ROCn RDMA | peer2peer
TensorRT | Tensile | 张量计算库
CUDA-Docker | ROCm-Docker | 

## Slide 21: HIP (Heterogeous-compute Interface for Portability，异构计算可移植接口)
HIP 可以说是 CUDA API 的”山寨克隆“版。除了一些不常用的功能（e.g. managed memory）外，几乎全盘拷贝 CUDA API，是 CUDA 的一个子集。
AMD 提供的 HIPify 工具，核心只是一个 perl 脚本，主要功能就是查找与替换。
HCC 是 基于 CLANG/LVVM 的开源编译器，是 ROCm 中 NVCC 的对应工具。相比于 NVCC，HCC 的提供了更多的功能 。HCC 单一编译环境统一支持 ISO C++ 11/14、C14、OpenMP 4.0，并且前向性的支持 C++17 “Parallel STL”，兼容 C++ AMP（微软推出的并行计算 API 标准），而且是同时适用于CPU、GPU。
rocBLAS 接口上兼容 Netlib BLAS 和 cuBLAS-v2 API。
随机数库 hcrng（HC Random Number Generator）
rocFFT 接口设计上与 clFFT 一致。

## Slide 22
Notes: https://www.coolaler.com/threads/amd-next-horizon7nm.353166/

## Slide 24: HSA support in AMD GPUs & Software
Notes: Reference:
GCN Native ISA LLVM Code Generator -- https://rocm-documentation.readthedocs.io/en/latest/ROCm_Compiler_SDK/ROCm-Native-ISA.html

## Slide 25: THANK YOU