## Slide 1: Understand of Chromium OS
Alan Zhang

## Slide 2: Background of Portage
Portage is a package management system used by Gentooto to install, uninstall and maintain software on your system from the source code.
The Portage system consists of:
  Portage tree which is a collection of ebuilds, that is a local copy (unzipped, and located in /usr/portage/) of the central ebuild repository, this default Portage tree can be sync'ed from official site via "emerge --sync" command that will sync the local Portage tree with the upstream Portage tree. Whenever you install software on your system with the emerge command, the Portage tree is searched. If a matching package name is found, its dependencies are calculated, the source code for the package and its dependencies are downloaded and then they're all compiled and installed onto your system.
    Portage 树有四层结点。根结点便是 /usr/portage 目录，第 2 层结点是软件包所属分类目录，第 3 层结点是软件包的名称目录，叶子结点则是 ebuild 文件以及其他辅助性文件或目录。以 gnome-shell-3.12.2.ebuild 文件为例，它在 Portage 树中的完整路径是 /usr/portage/gnome-base/gnome-shell/gnome-shell-3.12.2.ebuild。
    Ebuild: a specialized BASH script to give a set of instructions to emerge as an interface to the Portage software management system. Each version of each application or package in the Portage repository has a specific ebuild script written for it.
    Eclass: An eclass is a collection of code which can be used by more than one ebuild. three kinds of eclass:
      Those which provide common functions which are used by many ebuilds (for example, eutils, versionator, cvs, bash-completion)
      Those which provide a basic build system for many similar packages (for example, vim-plugin, kde)
      Those which handle one or a small number of packages with complex build systems (for example, vim, toolchain, kernel-2)
  emerge command: Executes the instructions in ebuilds (special scripts) in a sandbox environment;
  The Portage configuration files;
  The third-party Portage / emerge tools.
Notes: An eclass is roughly the equivalent of a library or header for an ebuild. Eclass is written in Bash just like ebuilds, and can be included in ebuilds file to share common codes. One example of an eclass specific to Chromium OS is cros_workon.
emerge acts as package manager like “apt” in ubuntu, but in Chromium OS build system, i.e. the Portage. For example, emerge-armgeneric vim, to bring vim into ARM target filesystem. With option “--unmerge”will remove a package from the targeet filesystem.

## Slide 3: Equery
Equery can be used to collect a variaty of information from Portage. Some common usages are:
  equery belongs <file>: tells you what package a file come from
  equery which <package>: tells you which ebuild is used for a package
  equery depends <package>: tells you what pakages are dependent on a package
  equery files <package>: tells you what files installed belonging to a particular package
  equery uses <package>: tells you what USE flags are enabled for a package
  equery-$BOARD g <package-name>: Show the dependency graph for a package

## Slide 4: Overlay Mechanism in Portage Tree
Portage 树支持一种被称为 Overlay 的技术。简单来说，就是我们可以另行建立一棵新的 Portage 树，这棵树的规模虽然比官方的 Portage 树小很多，但是 Portage 树的管理系统可以将这可新的 Portage 树与官方 Portage 树『合并』。如果新的 Portage 树中某些结点与官方的 Portage 树存在重叠，那么 Portage 树的管理系统会以前者覆盖后者，因此我们新建的 Portage 树通常被直呼为『Overlay』。

## Slide 5: Overlays in Chromium OS
Notes: There are multiple potential overlays locations, depend on if overlay contents are public, private, and/or a variant of a base board.
The locations in order of inclusion are:
* src/overlays/overlay-<board>
* src/overlays/overlay-variant-<board>-variant
* src/private-overlays/overlay-<board>-private
* src/private-overlays/overlay-variant-<board>-<variant>-private
$willis : tells you what is up in the chroot env.

## Slide 6: Establish Private Overlay
假设在 /usr/local 目录中创建自己的 Overlay，约定俗成的方式是： mkdir –p /usr/local/portage
需要将 Overlay 路径告知 Portage 管理系统，即在 /etc/make.conf 文件中添加以下代码： PORTDIR_OVERLAY = “/usr/local/portage”
为了让我们的 Overlay 能够被 Portage 管理系统所接受，需要在 /usr/local/portage 中创建 metadata 子目录，并在该目录内添加内容为 masters = gentoo 的 layout.conf 文件[1]，即：
  mkdir /usr/local/portage/metadata
  echo “masters = gentoo” > /usr/local/portage/metadata/layout.conf
最后，还需要在 `/usr/local/portage 中创建 profiles 子目录，并在该目录内添加 repo_name 文件。我们可以在这份文件中设置 Overlay 名称，只需将 Overlay 名称写入该文件即可。例如，我将我的 Overlay 命名为 garfileo：
  echo “garfileo” > /usr/local/portage/profiles/repo_name
Notes: A primary overlay contains:
* profiles/repo_name: Unique name
* make.conf: Defines build info
* toolchain.conf: Defines the toolchain
* There maybe also metadata/layout.conf: Defines the masters list for repositories which allows for disambiguation.

## Slide 7: Ebuild Syntax Used in Overlays
Variables
Column1 | Column2
EAPI | A version defined in ebuilds and other package manager related files which inform the package manager about the file syntax and content. It is, in effect, the version of the package manager specification (PMS) that the file adheres to.
S | The source directory for your package; commonly ${WORKDIR}/${P}. Portage will default to this value so you may not have to set it!
SLOT | Portage handles different versions of the same installed programs. If you would want, say GCC 2.95 and GCC 3.2 installed at the same time, you would specify the SLOT in each ebuild. Here we would set the SLOT of GCC 2.95 to 2 while we would set the SLOT of GCC 3.2 to 3. Note: Using 0 as the SLOT value signifies that this package only has 1 SLOT setting (in other words, this package is not SLOTable).
LICENSE | This variable specifies what license the program is covered under, i.e. GPL-2, BSD, etc... This field must be set to a valid license (which is any license found in /usr/portage/license/). If the license does not already exist there, it must be added before the ebuild can be added to the portage tree. If the license does not allow redistribution, make sure you placeRESTRICT="nomirror"intheebuild.
KEYWORDS | This variable now supports a couple of different functions. First of all, this variable specifies what architecture the ebuild is meant for. Some example keywords include: x86, ppc, sparc, mips, alpha, arm, hppa, amd64 and ia64. See the profiles/arch.list file in the Portage tree for more details. Obviously, you would set this to reflect the architecture of the target machine. Portage will not allow an x86 machine to build anything but x86, as specified by the KEYWORDS variable. Packages that do not support the native architecture are automatically masked by Portage. If the KEYWORDS flag has a preceding ~, then that indicates that the particular ebuild works, but needs to be tested in several environments before being moved to the stable profile with the given keyword. If the KEYWORDS flag has a preceding -,thenthepackagedoesnotworkwiththegivenkeyword.IfthereisnothingleadingKEYWORDS,thenthepackageisconsideredstable.YoucanallowinstallationofthesedifferenttypesofpackagesthroughtheACCEPT_KEYWORDSvariableinmake.conf.
DESCRIPTION | A short, one line description of your package.
IUSE | This is set to whatever USE variables your package utilizes. Remember that KEYWORDS should not be listed in here!
DEPEND | The package's build dependencies are listed here. See the section Package Dependencies for more details on proper syntax.
RDEPEND | The package's runtime dependencies are listed here. Once again, see Package Dependencies for more details.
Column1 | Column2
src_install | Use this function to install the package to an image in D. If your package uses automake, you can do this simply with emakeDESTDIR="${D}"install.MakesureyourpackageinstallsallitsfilesusingDastheroot!TheinitialworkingdirectoryisS.

## Slide 8: Hello World! for EBuild
假设在 app-misc 这个分类中有一个名为 hello-world 的软件包，现在我们要为这个软件包的 1.0 版的安装写一份 ebuild 文件。 注意：软件包的分类名并不是随意的，它必须要与 /usr/portage 中的某个子目录名一致。
首先在 Overlay 中建立软件包所在的分支：mkdir –p /usr/local/portage/app-misc/hello-world
可从 /usr/portage/header.txt 文件中获得 ebuild 文件默认的文件头，即：
  # Copyright 1999-2014 Gentoo Foundation
  # Distributed under the terms of the GNU ......
  可以直接将 /usr/portage/header.txt 文件复制为 hello-world-1.0.ebuild 文件，这样便可获得一个含有上述内容的空 ebuild 文件。ebuild 文件的名称必须符合 Portage 所认可的格式，即：软件包名称-版本号.ebuild。这一点很重要。
  cp /usr/portage/header.txt /usr/local/portage/app-misc/hello-world/hello-world-1.0.ebuild
  为这份ebuild文件增加以下内容: SLOT=“0”
接下来就是在这份文件上签名:
  cd /usr/local/portage/app-misc/hello-world
  ebuild ./hello-world-1.0.ebuild manifest // Manifest will be generated
继续向这份ebuild加入一些内容，
  EAPI=“5” // Portage系统已经为我们编写了许多有用的bash函数，设为5表示目前最新的bash函数。
  SLOT=“0” // 这个软件包的简述
  DESCRIPTION=“A classical example …” // 项目主页
  HOMEPAGE=http://wiki.Gentoo.org/index.html // 项目主页
  LICENSE=“MIT” // LGPL, MIT, GPL V2 …
  KEYWORDS=“~alpha ~amd ~arm ~hppa ~ia64 ~ppc ~ppc64 ~s390 ~x86”
一旦改动ebuild文件内容，那么必须重新生产Manifest文件: ebuild ./hello-world-1.0.ebuild manifest
使用emerge命令安装这个目前依然是子虚乌有的软件包: emerge –avt hello-world
Notes: Reference: https://segmentfault.com/a/1190000003819421
EAPI：Portage 系统已经为我们编写了许多有用的 Bash 函数，将 EAPI 的值设为 5 表示我们要用目前最新的 Bash 函数。这个变量必须要在 ebuild 文件头之后进行设定。
DESCRIPTION：这个变量存储了 hello-world 这个软件包的简介信息。
HOMEPAGE：定义了 hello-world 这个软件包的项目主页。
LICENSE：定义了 hello-world 这个软件包所使用的许可证，例如 LGPL，GPL V2，GPL V3，MIT 等。
KEYWORDS：如果你期望 hello-world 这个软件包能够安装在你的机器上，那么 KEYWORDS 变量的值必须要包含你在 /etc/make.conf 中所设定的 ACCEPT_KEYWORDS 值。
一旦改动了 ebuild 文件内容，那么必须重新生成 Manifest 文件：
# ebuild ./hello-world-1.0.ebuild manifest
现在，便可以使用 emerge 命令安装这个目前依然是子虚乌有的软件包了。

## Slide 9: Real “Hello World” Example
需要在hello-world-1.0.ebuild文件中添加: SRC_URI=http://xxxx/hello-world-1.0.tar.gz
重新生成Manifest是，ebuild.sh会自动下载源码到/usr/portage/distfiles中，并为这个源码也生成一个数字签名存储在Manifest文件中。
假设hello-world-1.0.tar.gz中只有一份bash脚本hello-world，那么没有编译需要，直接copy即可：
  src_install() {
    dobin hello-world
  }
  src_install是ebuild.sh能够识别并执行的函数名。该操作把hello-world拷贝到/usr/bin.
约定的内定义函数是以下面的次序执行的:

## Slide 10: depot_tools
Chromium uses a package of scripts, the depot_tools, to manage interaction with the Chromium source code repository and the Chromium development process. It contains the following utilities:
  gclient: Meta-checkout tool managing both subversion and git checkouts. It is similar to repo tool except that it works on Linux, OS X, and Windows and supports both svn and git. On the other hand, gclient doesn't integrate any code review functionality.
  gcl: Rietveld code review tool for subversion. The gcl tool runs presubmit scripts.
  git-cl: Rietveld code review tool for git. The git-cl tool runs presubmit scripts.
  hammer: (Obsolete) Wrapper script for building Chromium with the SCons software construction tool.
  svn [Windows only]: subversion client for Chromium development. (Executable Subversion binaries are included in the depot_tools on Windows systems as a convenience, so that working with Chromium source code does not require a separate Subversion download.)
  drover: Quickly revert svn commits.
  cpplint.py: Checks for C++ style compliance.
  presubmit_support.py: Runs PRESUBMIT.py presubmit checks.
  repo: The repo tool.
  trychange.py: Try server tool. It is wrapped by gcl try and git-try.
  git-try: Try change tool for git users
  wtf: Displays the active git branches in a chromium os checkout.
  weekly: Displays the log of checkins for a particular developer since a particular date for git checkouts.
  git-gs: Wrapper for git grep with relevant source types.
  zsh-goodies: Completion for zsh users.
Notes: http://dev.chromium.org/developers/how-tos/depottools

## Slide 11: Ninja
Ninja is yet another build system. It takes as input the interdependencies of files (typically source code and output executables) and orchestrates building them, quickly.

## Slide 12: cros_workon
cros_workon is a bash script that is used to select which portage packages you intent to work on.
The “cros_workon start” command will:
  Use the -9999 ebuild for a package;
  Build from local sources.
The “cros_workon stop” command will:
  Revert to the latest stable ebuild;
  Use prebuilt binaries when possible.
“cros_workon info, list and list-all” commands are useful.
When using cros_workon, two new commands are used instead:
  repo: Usually run outside the chroot.
    It's used to check out and sync your repositories and manage the tracking branches for git.
  src/scrips/cros_workon: Always run inside the chroot.
    It's used to unmask a package ebuild so that
    1) repo will be prepared to sync a local copy of the source, and
    2) build_packages will use the local source instead of the stable version.
Notes: Reference: https://www.chromium.org/chromium-os/developer-guide/developer-workflow
Ex.
cros_workon --board=${BOARD} --all list
Will list all packages that comply to the standards as following:
The ebuild for the package lives in the src/third_party/chromiumos-overlay or src/overlays/overlay-${BOARD} directories.
There is an ebuild for the package that ends with 9999.ebuild.
The ebuild inherits from the cros-workon class.
The ebuild has a KEYWORDS in the ebuild containing this architecture name (like "x86").

## Slide 13: What is a cros_workon package, and non cros_workon packages?
cros_workon package
  If an ebuild inherits cros_workon it is a cros_workon package.
  If you need to modify a cros_workon ebuild you must modify the -9999 version of the ebuild.
    When the change is submitted the builders will automatically up-rev the current stable ebuild and replace it with the contents of the -9999 ebuild.
Non cros_workon packages
  The package's ebuild file DOES NOT contain “inherit cros_workon” statement
  If so, “cros_workon” commands DO NOT work on this package.
  If you need to change an ebuild for a non cros_workon package then when submitting the change you will need to manually up-rev the ebuild.
    For example, git mv arbitrary-0.0.1-r3 arbitrary-0.0.1-r4
Pre-built
  The locations of the pre-builts is kept in : chromeos-partner-overlay/chromeos/binhost/target
Notes: cros_workon --board=${BOARD} start ${PACKAGE_NAME}
This command:
Indicates that you'd like to build the 9999 version of the ebuild instead of the stable, committed version.
Indicates that you'd like to build from source every time.
If you specified that you wanted the minilayout when you did your repo init, this command adds a clause to your .repo/local_manifest.xml to tell repo to sync down the source code for this package next time you do a repo sync.
After running cros_workon, sync down the sources via “repo sync” command executed from the outside of chroot, i.e. the ToT.
cros_workon --board=${BOARD} --all info | grep platform/ec
This command is to find out which ebuilds use for this source code from a specific directory, the command output are: chromeos-base/ec-utils chromiumos/platform/ec src/platform/ec
The name of the ebuild is chromeos-base/ec-utils
The path to the git repository on the server is chromiumos/platform/ec
The path to the source code on your system is src/platform/ec
equery-${BOARD} which ${PACKAGE_NAME}
This command finds out which ebuild file used for this specified package. Ex. platform/ec.

## Slide 14: Build Chromium OS
mkdir -p ~/workspace/chromiumos; cd ~/workspace/chromiumos
$repo init -u http://git.chromium.org/git/manifest -m minilayout.xml
$repo sync
$cd src/scripts
$./make_chroot
  To simplify dependencies, development is done inside a chroot. chroot 處於 ${HOME}/chromiumos/chroot。其中可以找到像 /usr/bin 和 /etc 這樣的系統目錄。這些對 chroot 是本地目錄，與您機器上的系統目錄相獨立。
$./enter_chroot.sh
  To enter the chroot in order to do development.
Or ./enter_chroot.sh --chrome_root=$(PATH/TO/CHROMIUM-BROWSER/SRC)
Or cros_sdk [--enter] # If existed chroot image file, it will mount chroot image, and enter it. 進入 chroot 時，會在 chroot 中裝載“~/trunk”目錄，它指向的就是 Chromium OS 主目錄 ${HOME}/chromiumos。
(cr)$ ./setup_board --board=x86-generic –default --job 4
  Run setup_board in order to install the toolchain (gcc/glibc) for the target you wish to work on. setup_board also creates the initial SYSROOT the target, 這將使用 /build/${BOARD} 的默認 sysroot 配置目標 board。
(cr)$./enable_localaccount.sh USERNAME
  The local user account allows login with no password even if you can not connect to the Internet.
(cr)$./set_shared_user_password.sh
  Need to set up the password for the shared "chronos" user, default password: test0000. The encrypted password will be stored in ./shared_user_password.txt.
(cr)$ ./build_packages --board="x86-generic" --jobs=4
  By default, build_packages will build the stable version of a package (i.e. from committed git sources) unless you are working on a package. If you are working on a package, build_packages will build using your local sources.
(cr)$ ./build_image --noenable_rootfs_verification
Or : USE='chrome_media' ./build_packages --board=amd64-generic --withautotest && USE='chrome_media' ./build_image --board=amd64-generic --boot_args "sched_debug ignore_loglevel debug verbose i915.preliminary_hw_support=1 console=ttyS2,115200n8" --noenable_rootfs_verification base dev test
Notes: Reference: http://l.lidian.info/zh-hant/Chromium_OS/developer_guide
首次執行 build_packages 將下載約 1.7GB 的源碼包與 1.3GB 的二進制程序包。更多關於 build_packages 到底做了什麼的信息請參看這裡。總之它會嘗試下載現有程序包來避免進行編譯（並將它們放在 /build/${BOARD}/packages 以備後續使用）。如果沒有程序包可下載，則會下載源碼包(並將它們放在 /var/lib/portage/distfiles-target）並編譯它們。
通常，build_packages 將編譯穩定版的軟件包（如根據已 commit 的 git 源），除非您在開發軟件包（帶 cros_workon）。 如果您在開發軟件包，build_packages 將使用您本地的源碼進行編譯。 關於cros_workon 的信息請參見下文。
邊注：--oldchromebinary 標記不是必需的，但在某些罕見的情況下（當 Chrome/Chromium 瀏覽器近期有修訂時）可以讓您的編譯更快，但代價是 Chrome/Chromium 的版本稍舊。 這在將來可能會成為默認選項。
邊注：即使有一些標記可優化編譯（如 --nowithdev、--nowithautotest 等），您也不應當使用它們（即使您不打算編譯開發/測試映像）。如果您使用了這些選項，還有些虛擬軟件包問題可能會導致一些難以調試的差異。
build_packages 步驟完成之後，您就可以通過在 ~/trunk/src/scripts 目錄中執行該命令創建映像文件了：
./build_image --board=${BOARD} --withdev --noenable_rootfs_verification
這將創建帶有可讓您自由修改 root 文件系統的開發工具的映像。 生成的映像不是安全的 Chromium OS 版本，但可以給您相對自由的訪問。 如果您想要更安全、加鎖版的 Chromium OS，可以去掉 --withdev 與 --noenable_rootfs_verification 選項。
build_image 所生成的映像位於 ~/trunk/src/build/images/${BOARD}/versionNum/（其中 versionNum 代表實際的版本號）。 為給定 board 生成的最新映像將被創建成符號鏈接 ~/trunk/src/build/images/${BOARD}/latest。

## Slide 15: Examples of Use Cases
Flash bootable and installation Chromium OS Built Image
  $./image_to_usb.sh --from=../build/images/x86/Version.BuiltDate&Time --to=/dev/USB-Node
  Or cros flash usb:// ../build/images/reef/latest
  “USB-Node” should be like “/dev/sdc” other than “/dev/sdc1”
Start working on specific package
  $./cros_workon --board=${BOARD} start ${PACKAGE_NAME} : This marks the ebuild for the given package so that build_packages will use your local changes instead of the stable, committed version.
  $ ./cros_workon --board=${BOARD} --all list : Check all the available packages; Special case : chromiumos-overlay is not in this list and cros_workon start/stop is not used.
Stop working on specific package
  $ ./cros_workon --board=${BOARD} stop ${PACKAGE_NAME} : This tells the buildsystem to use stable pre-built version of the package. build_packages will now ignore your local repository. Stopping doesn't delete your local copy.
Autotest
  $ ./cros_workon start autotest autotest-tests
  $ repo sync
  Tests consist of a build phase and run phase, where the first is executed by the ebuild, and the second by the run_remote_tests.sh" script. tests have to be built with emerge-${board} before they can be ran using run_remote_tests.sh.
  Currently, tests are organized within these ebuilds : chromeos-base/autotest-tests
  To see which tests are implemented by an ebuild, run the usual pretended emerge:
  $ emerge-${board} -pv autotest-tests
  All tests have a default state, either enabled (+) or disabled (-). The TESTS= variable is a USE_EXPAND.
  There are two ways to use these.
  (1) Non-Incremental --- Simply override the list by a new list
  TESTS="platform_MiniJailPidNamespace platform_MiniJailPtraceDisabled" emerge-${board} -pv autotest-tests
  (2) Incremental --- All USE_EXPAND flags are also accessible as USE flags, with the appropriate prefix, and can be used incrementally with +, -
  USE="tests_platform_MiniJailPidNamespace tests_platform_MiniJailPtraceDisabled" emerge-${board} -pv autotest-tests
Notes: https://www.chromium.org/chromium-os/developer-guide/developer-workflow
https://sites.google.com/a/chromium.org/dev/chromium-os/chromiumos-design-docs

## Slide 16: Chrome Web Apps
Apps
  hosted app
  packaged app
Themes
Extensions
Remote Desktop Capabilities - Chromoting
GPU Accelerated Compositing – WebGL
  WebGL is a cross-platform, royalty-free API used to create 3D graphics in a Web browser. Based on OpenGL ES 2.0, WebGL uses the OpenGL shading language, GLSL, and offers the familiarity of the standard OpenGL API.
  Chromium must be launched from the command line in order to enable WebGL.
  Linux : ./chrome --enable-webgl
  Mac OS X : ./Chromium.app/Contents/MacOS/Chromium --enable-webgl
  Windows : No command line options needed.

## Slide 17: Firmware
Functionalities
  System recovery
  Verified boot
  Fast boot

## Slide 18: 淺談 Malicious Engine https://v2bv.net/2017/intel-me
什麼是 ME？
  Intel ME 是 Intel Management Engine 的簡稱。
  Intel ME 是一個擁有從底層控制硬件能力的、獨立與處理器和操作系統的框架，它對於操作系統也是隱形的。簡單點說就是擁有極高的權限。其中 Intel Active Management Technology（英特爾主動管理技術）是運行與 ME 框架上的應用的一個例子。
  Intel ME 被搭載在幾乎所有的 2006 年之後上市出售的 intel 平臺上。硬件部分整合在 CPU 或是主板芯片組內；軟件（固件）部分一般與 BIOS 共存在一個 ROM 芯片中（如果把 ROM 的內容提取出來的話，會發現 ME 固件往往比 BIOS 本身以及 GBE 固件加在一起還大）。
  在 Linux 平臺上可以使用 intelmetool 來查看 ME 的狀態。
Notes: Reference :
For ME firmware: https://v2bv.net/2017/intel-me

## Slide 19: 使用coreboot (1/6) https://v2bv.net/2018/coreboot
編譯 coreboot 的依賴裝好,gcc,gnat,bison,flex,ncurses,wget,zlib
coreboot 的源碼拖下來:
  $ git clone https://review.coreboot.org/coreboot.git
  $ cd coreboot && git submodule update --init --checkout
  $ git clone https://review.coreboot.org/flashrom.git
進入 coreboot 的源碼目錄裏，準備好工具鏈等等：
  $ make crossgcc-i386 CPUS=4 # 這裏只需要給 X220 用，所以準備 i386 的工具鏈就足夠了
  $ make iasl # 準備 iASL 編譯器
用 flashrom 把現有的固件 Dump 出來：
  $ sudo flashrom -p internal:laptop=force_I_want_a_brick -c MX25L6405D -r dump.rom # 這裏舉例用的是 internal flash 的命令，如果用編程器的話需要根據編程器進行修改。
進入 coreboot 源碼目錄的 util/ifdtool 目錄下並編譯它：
  $ cd util/ifdtool && make
使用 ifdtool 解鎖固件描述（firmware descriptor）和 ME 區域。
  $ ifdtool -u dump.rom # 把文件名改成自己的, ifdtool 會創建一個新的 dump.rom.new，接下來的步驟要用它。
想幹掉 ME 的話現在拿去過一邊 me_cleaner 應該就可以刷回去了。
  $ me_claner.py dump.rom.new # 換成你自己的文件名
進入 flashrom 源碼目錄下的 util/ich_descriptors_tool 目錄並編譯 ich_descriptors_tool
  $ cd util/ich_descriptors_tool && make

## Slide 20: 使用coreboot (2/6) https://v2bv.net/2018/coreboot
然後用它來提取文件：
  $ ich_descriptors_tool -f dump.rom.new -d # 當然，還是要改成自己的文件名. 這個工具會輸出一大堆東西，我們只要它創建的 dump.rom.new.Descriptor.bin、dump.rom.new.ME.bin 和 dump.rom.new.GBE.bin,分別代表着需要用到的三大坨 blob。
然後我們可以把這些文件複製到 coreboot 源碼目錄的 3rdparty/blobs 目錄的對應位置裏（這是爲了之後配置起來方便點）。
  $ cp dump.rom.new.Descriptor.bin ~/coreboot/3rdparty/blobs/mainboard/lenovo/x220/descriptor.bin
  $ cp dump.rom.new.ME.bin ~/coreboot/3rdparty/blobs/mainboard/lenovo/x220/me.bin
  $ cp dump.rom.new.GBE.bin ~/coreboot/3rdparty/blobs/mainboard/lenovo/x220/gbe.bin

## Slide 21: 使用coreboot (3/6) https://v2bv.net/2018/coreboot
接下來就是配置 coreboot, 回到 coreboot 的源碼目錄下執行 make menuconfig 開始配置。
進入第一個 General setup，
  [*] Generate flashmap descriptor parser using flex and bison
  [*] Generate SCONFIG & BLOBTOOL parser using flex and bison
  [*] Use CMOS for configuration values
  [*] Compress ramstage with LZMA
  [*] Include the coreboot .config file into the ROM image
  [*] Create a table of timestamps collected during boot
  [*] Allow use of binary-only repository # 這條一定要打開
  -*- Build the ramstage to be relocatable in 32-bit address space.

## Slide 22: 使用coreboot (4/6) https://v2bv.net/2018/coreboot
之後是 Mainboard，
  *** Important: Run 'make distclean' before switching boards ***
  Mainboard vendor (Lenovo) ---> # 選聯想
  Mainboard model (ThinkPad X220) ---> # 當然是 X220 啦
  ROM chip size (8192 KB (8 MB)) ---> # 除非你魔改過，不然不用改
  (0x100000) Size of CBFS filesystem in ROM
  () fmap description file in fmd format
然後 Chipset：
  [*] Enable VMX for virtualization
  [*] Set lock bit after configuring VMX
  -*- Use native raminit
  [*] Beep on fatal error
  [*] Flash LEDs on fatal error
  [*] Support bluetooth on wifi cards
  *** Intel Firmware ***
  [*] Add Intel descriptor.bin file # 必選
  [*] Add Intel ME/TXE firmware # 必選
  (3rdparty/blobs/mainboard/$(MAINBOARDDIR)/me.bin) Path to management engine firmware # 同上
  [*] Verify the integrity of the supplied ME/TXE firmware
  [*] Strip down the Intel ME/TXE firmware # 如果要幹 ME 的話選上這個
  *** Please test the modified ME/TXE firmware and coreboot in two steps ***
  [*] Add gigabit ethernet firmware # 必選

## Slide 23: 使用coreboot (5/6) https://v2bv.net/2018/coreboot
Devices 裏：
  -*- Enable PCIe Common Clock
  -*- Enable PCIe ASPM
  [*] Enable PCIe Clock Power Management
  [*] Enable PCIe ASPM L1 SubState
  [*] Enable I2C controller emulation in software
Generic Drivers 裏基本不需要動:
  [*] SPI flash driver support in SMM
  [*] Support Intel PCI-e WiFi adapters
  [*] PS/2 keyboard init # 必選
  [*] Enable TPM support # 如果需要 TPM 的話可以選上
Security 下沒需求的話就不用改了：
  Verified Boot (vboot) --->
  [ ] Verify firmware with vboot.
Console 裏：
  [*] Squelch AP CPUs from early console.
  [*] Send POST codes to an IO port
System Table：
  [*] Generate SMBIOS tables
Payload 裏比較特殊，需要根據自己的需求選擇 _(:з」∠)_。現在官方支持的 Payload 有：
  None - 無，什麼都沒有。
  An ELF executable payload - 一個 ELF 可執行文件作爲 Payload。
  Bayou - 一個可以從 CBFS（coreboot filesystem）裏選擇並啓動別的 payload 的工具（是不是有點繞）。
  FILO - 一個啓動管理器，比較簡單的那種。
  GRUB2 - 知名啓動管理器。
  SeaBIOS - 一個開源的 BIOS 實現，爲默認選項。
  U-Boot - 熟悉 ARM 的朋友應該知道（跑A Linux payload - 直接把一個 Linux 內核作爲 payload 塞進去。
  Tianocore coreboot payload package - 開源的 UEFI 實現。

## Slide 24: 使用coreboot (6/6) https://v2bv.net/2018/coreboot
全部配置好之後保存然後退出。使用 make,編譯好的固件在源碼目錄的 build/coreboot.rom。
進入 build 目錄下就可以用 flashrom 刷了。
  $ sudo flashrom -p internal:laptop=force_I_want_a_brick -c MX25L6405D -w coreboot.rom # 同樣的，這裏的命令也是 internal flash 的命令，如果用編程器的話需要根據情況進行修改。
如何配置 GRUB2
  GRUB2 需要一個配置文件才能正常工作，詳細情況可以參考 https://github.com/hardenedlinux/Debian-GNU-Linux-Profiles/blob/master/docs/hardened_boot/grub-for-coreboot.md
  幾個注意點：
    一些經常變動的東西可以寫到硬盤上讓 GRUB 自己去加載，而不是寫到固件裏面。
    (memdisk) 和 (cbfsdisk) 要區分清楚，(cbfsdisk) 是 ROM 裏的 CBFS 區域，而 (memdisk) 是 grub-mkstandalone 時包括進去的部分。
    如果圖形相關選擇的是 native init 的 high-resolution framebuffer，並且進去後發現只有四分之一個屏幕可用的話可以試着在配置裏加上 gfxpayload=keep 和 terminal_output --append gfxterm，應該可以讓它恢復正常。
Notes: Assemble GRUB executable for coreboot: https://github.com/hardenedlinux/Debian-GNU-Linux-Profiles/blob/master/docs/hardened_boot/grub-for-coreboot.md

## Slide 25: Set up GPIO in Coreboot
Two roles involving GPIO manipulation, one is pinctrl, the other is gpiolib; pinctrl cross-correlates the GPIO numbers (which are a global business) to a certain pin on a certain pin controller that is described in “pinctrl.txt”. gpio drivers announce their pin ranges to the pin ctrl subsystem before it will call 'pinctrl_request_gpio' in order to request the corresponding pin to be prepared by the pinctrl subsystem before any gpio usage, For this, the gpio controller can register its pin range with pinctrl subsystem. There are two ways of doing it currently: with or without DT.
For with DT support refer to Documentation/devicetree/bindings/gpio/gpio.txt.
For non-DT support, user can call gpiochip_add_pin_range() with appropriate
parameters to register a range of gpio pins with a pinctrl driver.
Notes: Reference:
https://android.googlesource.com/platform/hardware/bsp/kernel/intel/+/edison-3.10/Documentation/gpio.txt

## Slide 26
In Linux GPIO framework, there are 2 modules for GPIO function. One is pinctrl module that defines the PAD usage per ACPI "INT3452" table's definition, the other is GPIOLIB that provides gpio_xxx kernel layer APIs to other program. In your Apollo Lake platform, the logic is the following:
1. Coreboot phase
File: src/mainboard/google/reef/variants/coral/gpio.c, that is the Pad configuration in ramstage.
PAD_CFG_GPI_APIC_LOW(GPIO_21, NONE, DEEP), /* Touch IRQ */
File: src/mainboard/google/reef/variants/coral/devicetree.cb
register "hid" = ""ELAN0001""
register "desc" = ""ELAN Touchscreen""
register "irq" = "ACPI_IRQ_EDGE_LOW(GPIO_21_IRQ)"
2. Linux pinctrl module phase
static const struct intel_pinctrl_soc_data bxt_north_soc_data = {
.uid = "1",
.pins = bxt_north_pins,
.npins = ARRAY_SIZE(bxt_north_pins),
.groups = bxt_north_groups,
.ngroups = ARRAY_SIZE(bxt_north_groups),
.functions = bxt_north_functions,
.nfunctions = ARRAY_SIZE(bxt_north_functions),
.communities = bxt_north_communities,
.ncommunities = ARRAY_SIZE(bxt_north_communities),
}; /* PINCTRL_PIN(21, "GPIO_21"), is defined */
Define "INT3452" ACPI label that will be probed by ACPI driver, so the PIN configuration will be settled down.
3. GPIOLIB module
Pls reference kernel/Documentation/gpio/board.txt to understand the kernel level GPIO APIs that are very few, and used by other Linux kernel drivers. The export to userspace manipulation interface are :
/sys/class/gpio# echo 44 > export
/sys/class/gpio/gpio44# echo out > direction
/sys/class/gpio/gpio44# cat direction
/sys/class/gpio/gpio44# echo 1 > value
/sys/class/gpio/gpio44# cat value
/sys/class/gpio# echo 44 > unexport

## Slide 27: Build Firmware of Coreboot, and EC for Carol
Sync coreboot code
  export REPO_HOST_PORT_INFO="chromium.XXXXXXX.com 418"
  mkdir ~/workspace/ldev-consolidated_01
  cd ~/workspace/ldev-consolidated_01
  repo init -u ssh://chromium.XXXXXXX.com/chromiumos/manifest-mirror.git
  repo sync
Build coreboot with Intel FSP
  cros_sdk --enter
  ./setup_board --board=carol
  cros_workon-carol start coreboot depthcharge libpayload vboot_reference chromeos-bootimage chromeos-mrc
  # FSP build
  USE="fsp_src" emerge-carol sys-boot/chromeos-mrc
  # Coreboot build
  emerge-carol coreboot coreboot-private-files-carol depthcharge libpayload vboot_reference chromeos-bootimage
  NOTE: There can be build errors if the error is because of the missing file "ec.RW.bin"
  sudo touch /build/carol/firmware/ec.RW.bin; sudo touch /build/carol/firmware/ec.RW.bin, and re-run the emerge step.
  your output image is /build/carol/firmware/image.*.bin. Flashing the image.bin under /build/carol/firmware directory on to SPI via dediprog.
Build EC Firmware
  cros_workon-carol start chromeos-ec
  emerge-carol chromeos-ec
Notes: Skylake FSP to coreboot integration overview: https://www.youtube.com/watch?v=SpL8LbquSVs&t=4s
Port Coreboot to a new board: https://www.youtube.com/watch?v=8wPskpLHFIo&t=17s
Port Coreboot to x86 platform: https://www.youtube.com/watch?v=HKJNJh6JW_Y&t=31s
Depthcharge: The Chromium OS Bootloader: https://www.youtube.com/watch?v=6ZKeDGI75vw&t=369s
Chrome OS Embedded Controller: https://www.youtube.com/watch?v=Ie7LRGgCXC8
Summit:
https://www.chromium.org/chromium-os/2014-firmware-summit

## Slide 28: How to Change Date Time inside Chromium OS

## Slide 29: How to share files for inside and outside chroot
The cros_sdk command supports mounting additional directories into your chroot environment. This can be used to share editor configurations, a directory full of recovery images, etc.
You can create a src/scripts/.local_mounts file listing all the directories (outside of the chroot) that you'd like to access inside the chroot. For example:
  # source(path outside chroot) destination(path inside chroot)
  /usr/share/vim/google
  /home/YOURID/Downloads /Downloads
Each line of .local_mounts refers to a directory you'd like to mount, and where you'd like it mounted. For security and safety reasons, all directories mounted via .local_mounts will be read-only.
Reference: http://dev.chromium.org/chromium-os/tips-and-tricks-for-chromium-os-developers

## Slide 30: General Development Tasks on Chromium OS
Repo chromium os codebase
  Install depot_tools and repo sync init and sync chromium codebase
  cros_sdk # Bring you to the chroot environment
  (cr) $ export BOARD=your_platform_name
  (cr) $ ./setup_board --board=your_platform_name --nousepkg
  (cr) $ ./build_packages --board=your_platform_name --nousepkg
  (cr) $ ./build_image --board=your_platform_name --noenable_rootfs_verification test --boot_args='earlyprintk=serial,ttyS0,115200 console=ttyS0,115200 loglevel=8'
Updating your device using USB
  (cr) $ ./image_to_usb.sh --board=your_platform_name --to=/dev/sdd --from=../build/images/your_platform_name/Chromium...
  Or: (cr) $ cros flash usb:// /path/to/*image.bin
Boot from USB
  Option 1: On the device, goto recovery mode by pressing Esc + Refresh (aka the third function key from left) + Power and then insert your USB drive
  Option 2: While booting up, if you are in developer mode, it displays a screen with red text that you are in developer mode and press Ctrl+U to boot from USB. Press Ctrl+U
Enter dev shell
  Option 1: After booting completes, press Ctrl + Alt + F2 to go to the dev shell (Note, this was broken in some releases)
  Option 2: Login as guest if you have not set up any account yet, else login with your account. Launch browser, press Ctrl+Alt + T, you get a chrome shell. Type shell to get a dev shell
Login with chronos or root and run the following command. (If built in test mode, as of now the pwd is test0000.)
  $ sudo chromeos-install --dst /dev/mmcblk0

## Slide 31: How to add private overlay for specific platform (1/2)
Assumption: chromium-os source pool, here is a short note to build image for your_platform_name
  $ cd .repo
  $ mkdir -p local_manifests
  $ cd local_manifests
  $ vim local_manifest.xml # includes the following lines:
    <?xml version='1.0' encoding='UTF-8'?>
    <manifest>
    <remote name="Alias Name of My Remote Server" fetch="URL of this remote server. ex. https://chromium.xxxx.com" review="URL of this remote server. ex. https://chromium.xxxx.com"/>
    <project name="chromeos/overlays/overlay-your_platform_name-private" path="src/private-overlays/overlay-your_platform_name-private" remote="Alias Name of My Remote Server"/>
    </manifest>
  Back to ToT, "cd ../..; repo sync"
  Build packages and images # Refer to page 27
  Examine built images
    (cr) $ ./mount_gpt_image.sh --board=${BOARD} -f $(./get_latest_image.sh --board=${BOARD})
    (cr) $ # Do something you'd like to check
    (cr) $ ./mount_gpt_image.sh --board=${BOARD} -u # remember to umount
    Note: If you built test image (./build_image.sh .... test ), do not use get_latest_image.sh script, append the path of chromiumos_test_image.bin directly

## Slide 32: How to add private overlay for specific platform (2/2)
Test your images on QEMU (optional)
  Assume you have QEMU at system-wide ($ sudo apt-get install qemu-kvm), and remember to turn on visualization in BIOS
  Build image for QEMU (inside chroot)
    (cr) $ ./image_to_vm.sh --from=../build/images/your_platform_name/latest --board=${BOARD}
    Launch QEMU with image (outside chroot)
    $ sudo kvm -m 2048 -hda src/build/images/auron/latest/chromiumos_qemu_image.bin -net nic,model=e1000 -net user
    (cr) $ sudo qemu-system-x86_64 -enable-kvm -m 1024 -cpu Broadwell -net nic,model=e1000 -net user -hda /mnt/host/source/src/build/images/fox_wtm2/latest/chromiumos_qemu_image.bin
    Note: Unlike system-wised QEMU, the one in cros_sdk uses VNC server, hence you need to get a VNC viewer, you could use VNC Viewer app

## Slide 33: How to Configure Bluetooth Device ID
First identify the appropriate overlay for the board or variant, this is usually in
src/overlays/overlay-$BOARD but for devices still in development this may be in
src/private-overlays/overlay-$BOARD-private within the Chrome OS internal checkout.
The overlay should contain a "bsp" package, in chromeos-base/chromeos-bsp-$BOARD, with an
accompanying files directory. Do not mistake this for the "chromeos-bsp-$BOARD-private" overlay,
which does not generally have accompanying files.
Add a file called main.conf to the files directory containing the following:
[General]
DeviceID = bluetooth:00E0:XXXX:0400
Modify the ebuild file for the bsp package, adding to the src_install section:
# Install Bluetooth ID override.
insinto "/etc/bluetooth"
doins "${FILESDIR}/main.conf"
Don't forget to rename the ebuild symlink to increase the revision number.
Run "bt_console" from the crosh shell and use the show command to show information about the local adapter. At this step you can also verify that the information in the local adapter is correct. The output from show, in addition to the Bluetooth address, should contain the line:
Modalias: bluetooth:v00E0p XXXX d0400

## Slide 34: How to Add New Driver into Chromium Build System
1. Prepare a simple driver
~/chromiumos/src/third_party/kernel/v3.10/drivers
2. Add the hello config to chrome build system
~/chromiumos/src/third_party/chromiumos-overlay/eclass
3. Modify the customized YourPlatformName config
~/chromiumos/src/overlays/overlay-YourPlatformName
4. Make & update kernel
emerge-YourPlatformName chromeos-kernel-3_10 && update_kernel.sh --remote=$IP
5. For debug, use "dmesg | grep Hello"

## Slide 35: Vital Product Data (VPD)
Region in Read-Only and Read-Write flash
RO_VPD
Serial Number
Initial Locale
Initial Time Zone
Keyboard Layout
RW_VPD
Activation Date
Registration Codes
Tool: vpd
Display contents of read-only VPD
  # vpd -i RO_VPD -l
Display contents of read-write VPD
  # vpd -i RW_VPD -l
Erase and reformat read-only VPD
  # vpd -i RO_VPD -O
Add serial number to read-only VPD
  # vpd -i RO_VPD -s serial_number=1234567890
Read back serial number value
  # vpd -i RO_VPD -g serial_number

## Slide 36: Examine eMMc in Chromium Runtime Env
Device info
  Inside Chromium OS runtime environment, review the eMMC device information via /var/log/storage_info.txt
  CL Reference: https://chromium-review.googlesource.com/c/chromiumos/platform/depthcharge/+/238101
Host info - cat /sys/kernel/debug/mmc0/
Throughput
  Read: hdparm -Tt --direct /dev/mmcblk0
  Write:
    localhost ~ # cd /mnt/stateful_partition
    localhost ~ # temp=`uuidgen`; dd if=/dev/zero of=${temp} conv=fdatasync bs=4k count=100k; rm ${temp}

## Slide 37: How-To Chromium OS Kernel Tracing
# cd /sys/kernel/debug/tracing
# echo function > current_tracer
# cat trace # this dumps current trace buffer
# echo nop > current_tracer
There is one tip you can dump the trace buffer while panic, along with Oops message, either using sysctl or /proc
# cd /proc/sys/kernel
# echo 1 > ftrace_dump_on_oops
Notes: Reference:
https://lwn.net/Articles/365835/
https://lwn.net/Articles/366796/

## Slide 38: Chromium OS Performance Tuning
Ftrace is the famous Linux kernel profiling tool. UXTune is based on Ftrace.
Mount the debugfs filesystem
  mount -t debugfs none /sys/kernel/debug
Enter the ftrace the working directory
  cd /sys/kernel/debug/tracing
Start to capture data using the "function" tracer
  echo 0 > /sys/kernel/debug/tracing/tracing_enabled
  echo 1 > /proc/sys/kernel/ftrace_enabled
  echo function > /sys/kernel/debug/tracing/current_tracer
  echo 1 > /sys/kernel/debug/tracing/tracing_on
  echo 1 > /sys/kernel/debug/tracing/tracing_enabled
  ... your work ...
Start to capture data using the "function graph" tracer
  echo function_graph > /sys/kernel/debug/tracing/current_tracer
Stop and view data
  echo 0 > /sys/kernel/debug/tracing/tracing_enabled
  cat /sys/kernel/debug/tracing/trace > data.file
  vi data.file
Examples by the "function graph" tracer
# tracer: function_graph
#
# CPU DURATION FUNCTION CALLS
# | | | | | | |
1) 2.964 us | sub_preempt_count();
1) 1.893 us | add_preempt_count();
1) 1.853 us | sub_preempt_count();
1) 1.883 us | add_preempt_count();
1) 1.833 us | sub_preempt_count();
1) 1.853 us | add_preempt_count();
1) 1.863 us | sub_preempt_count();
1) 1.803 us | add_preempt_count();
1) 1.863 us | sub_preempt_count();
1) 1.923 us | add_preempt_count();
1) 1.843 us | sub_preempt_count();
1) | add_preempt_count() {
1) ==========> |
1) | smp_apic_timer_interrupt() {
1) | apic_write() {
1) 2.414 us | native_apic_mem_write();
1) 6.420 us | }
1) | irq_enter() {
1) 1.913 us | rcu_irq_enter();
1) 1.773 us | idle_cpu();
1) 1.843 us | add_preempt_count();

## Slide 39: Script to reset TPM
The script need to run under "recovery mode".
#!/bin/sh
#
stop tcsd
tpmc ppon
tpmc clear
tpmc enable
tpmc activate
tpmc write 0x1007 2 0 1 0 1 0 0 0 0 0x4f
tpmc write 0x1008 2 4c 57 52 47 1 0 1 0 0 0 0 0x55

## Slide 40: How to use Crouton to run Ubuntu inside Chromium OS
Step 1. Enabling Developer Mode
Step 2. Installing Crouton
  Step 2.1 Download the latest release of Crouton to your Chromebook: http://goo.gl/fd3zc
  Step 2.2 Install Crouton with the Xfce desktop
Step 3. Run Ubuntu - sudo startxfce4
Step 4. OS switch
  Chrome OS -> Ubuntu : Alt+Ctrl+Shift+Back
  Ubuntu -> Chrome OS : lt+Ctrl+Shift+Forward
Advanced installation:
  sudo -i
  cd /home/user/{uuid}/Download
  List available target: sh ./crouton -t list
  List available release: sh ./crouton -r list
  Install Ubuntu 14.04 w/ Unity: sh ./crouton -t unity-desktop -r trusty
  Install Xfce w/ applications: sh ./crouton -t xfce-desktop
  Install LXDE w/ applications: sh ./crouton -t lxde-desktop
  Install GNOME w/ applications: sh ./crouton -t gnome-desktop
  Install KDE w/ applications: sh ./crouton -t kde-desktop

## Slide 41: Crostini
Crostini should supplant Crouton that you can run Android and Linux applications side-by-side with the familiar web browser environment of Chromium OS.
Enable VT-x configuration in firmware
Enabling Crostini is simple, switch to the developers channel, then go into settings, scroll down to Linux (Beta), and enable it that causes a download of the Crostini/Linux support, and away you go.
For news about Crostini: https://www.reddit.com/r/Crostini/
Crostini Wiki: https://old.reddit.com/r/Crostini/wiki/index
Notes: Reference:
https://techsparx.com/chromebooks/crostini/crostini-getting-started.html
https://www.reddit.com/r/Crostini/

## Slide 42: Running Custom Containers Under Chromium OS
Reference
  https://chromium.googlesource.com/chromiumos/docs/+/master/containers_and_vms.md#Quickstart
Natively Running Windows 7 on Acer C7 Chromebook
  https://www.youtube.com/watch?v=m5crPfEAhvs&t=38s
Notes: Reference:
https://mp.weixin.qq.com/s?__biz=MzI4MzAwNTQ3NQ==&mid=209866190&idx=1&sn=0ee75509eb2fab454009125e0a8c6437&scene=0#rd

## Slide 43: Chromium OS UI Framework
Chromium OS UI --> View --> Aura --> Xlib --> X Server // DRM/KMS --> i915 Device Driver
Chromium OS UI --> View --> Aura --> Ozone-gbm // DRM/KMS --> i915 Device Driver
Notes: Chromium OS GUI:
https://gitai.me/2017/03/18/gui-of-chromeos/
https://www.x.org/wiki/Events/XDC2016/Program/Arcpp_Graphics.pdf
Ozone Reference:
https://software.intel.com/en-us/blogs/2014/10/23/chromium-ozone-gbm-explained
https://chromium.googlesource.com/chromium/src/+/lkgr/docs/ozone_overview.md
初识Wayland（X、Mir）: http://os.51cto.com/art/201011/233447_all.htm
Direct Render Manager: https://wikivisually.com/wiki/Direct_Rendering_Manager
Reference on Computer Gfx: http://www.opengpu.org/forum.php?mod=viewthread&tid=326
要做一個投影，首先是攝影機(camera,或eye point)的位置，攝影機朝向的方向，攝影機的視角(包含上下與左右的開展角度)，攝影機的「上向量」(upvector)，近平面(near)，遠平面(far)。使用頂點(Vertex)組成網眼(Mesh)架構，來記錄三維的資料。一個Vertex可以帶有許多資料，稱作屬性(Attribute)，比如說該點在空間座標系中的座標(Coordinate)、法向量(Normal)、該點的顏色(Color)、紋理座標(Texture coord.)Vertex同時也可以作為貝茲曲面(Bezier surface)或NURBS曲面的control point。由頂點(Vertex)組成的結構稱為Mesh，這些線條說明了Vertex如何連結成為Mesh，我們稱作Primitive，注意Primitive並不是線條而是一個抽像的連結概念。最簡單的Primitive有三種，點、線、三角形。而這就是全部了，因為所有的多邊形都可以拆成三角形，關於這方面我會在之後討論硬體時再詳細的說明。於是Vertex與Primitive組成了一個3D scene，3DComputer Graphics領域中的兩個主題：Modeling與Rendering，分別是決定了從虛擬的場景概念到Vertex與Mesh，以及從Vertex與Mesh到螢幕上的pixel color這兩個階段。

## Slide 44: Linux DISPLAY=:0.0
在Linux/Unix類操作系統上, DISPLAY用來設置將圖形顯示到何處. 在終端上輸入printenv查看當前環境變量.
DISPLAY 環境變量格式如下host:NumA.NumB, host指Xserver所在的主機主機名或者ip地址, 圖形將顯示在這一機器上, 可以是啟動了圖形界面的Linux/Unix機器, 也可以是安裝了Exceed, X-Deep/32等Windows平台運行的Xserver的Windows機器. 如果Host為空, 則表示Xserver運行於本機, 並且圖形程序(Xclient)使用unix socket方式連接到Xserver, 而不是TCP方式. 使用TCP方式連接時, NumA為連接的端口減去6000的值, 如果NumA為0, 則表示連接到6000端口; 使用unix socket方式連接時則表示連接的unix socket的路徑, 如果為0, 則表示連接到/tmp/.X11-unix/X0 . NumB則幾乎總是0.
Notes: Reference: https://jerry2yang.wordpress.com/2011/10/05/linux-display0-0/