## Slide 1: Understanding 2LM/PM in Linux

## Slide 2: Agenda
Concept of Persistent Memory
Conceptual User Model of Persistent Memory in Linux
Persistent Memory in Runtime Environment
Architecture Model of Persistent Memory in Linux
Ecosystem and Industry Standards

## Slide 3: Concept of Persistent Memory
Persistent memory (or storage class memory, the synonymous) is media w/ byte-addressable, load/store memory access, but w/ the persistence properties of storage. Narrow down PM in Intel solution, it is the NVDIMM that connects to system memory bus.
Benefits as being operated in memory semantics
  High performance in transaction processing
  CPU cache coherency via standard APIs like fsync, msync w/o system page
  DMA
  Byte addressability to support fine granularity manipulation
Notes: with DAX the virtual address returned by mmap to the userspace application points to the persistent memory and not the page cache. This allows the userspace application to perform loads, stores and flushes directly to the persistent memory addresses, completely bypassing the page cache. For DAX these system calls cause the kernel to flush modified data cache lines in the processor caches out to the NVDIMMs.

## Slide 4: Persistent Memory User Model
Notes: NVDIMM Driver consumes NFIT (NVDIMM Firmware Interface Table) defined in ACPI ver.6.0 to enumerate NVDIMMs installed, then exposes the instantiated entity to management software, traditional block storage which is emulated by driver, and also persistent memory aware file system like ext4/5, XFS etc.

## Slide 5: Persistent Memory in Runtime (1)
Persistent memory aware file system works on DAX (Direct Access) that allows direct access to persistent memory w/o using the system page cache that is required for normal, storage-based files.
Persistent memory can be mapped into memory using standard APIs like mmap() as shown in right picture. No kernel involvement, no interrupts for kernel/user-space context switch, only involve NVDIMM driver.
To make runtime data persistent
  From CPU cache to Persistent Memory via msync() or fsync() calls, flush CPU cache data into persistent memory
  Via ADR (Asynchronous DRAM refresh) which is supported by NVDIMM and platform memory controller
Notes: NVDIMM Driver consumes NFIT (NVDIMM Firmware Interface Table) defined in ACPI ver.6.0 to enumerate NVDIMMs installed, then exposes the instantiated entity to management software, traditional block storage which is emulated by driver, and also persistent memory aware file system like EXT4/5, XFS etc.
DAX requires support from the underlying filesystem. It is currently supported by XFS, ext4 and ext2.

## Slide 6: Persistent Memory in Runtime (2)
Asynchronous DRAM Re-fresh (ADR)
Notes: Reference: https://www.snia.org/sites/default/files/SDC15_presentations/persistant_mem/JeffChang-ArthurSainio_NVDIMM_Cookbook.pdf
A platform-level feature where the power supply signals other system components that power-fail is imminent, causing the Write Pending Queues in the memory subsystem to be flushed.
Write Pending Queues in the memory subsystem.
Instructions that flush lines from the CPU caches. CLWB and CLFLUSHOPT are recent additions for better pmem performance

## Slide 7: x86 Instructions for Transaction Operation on Persistent Memory
Notes: Instructions that flush lines from the CPU caches. CLWB and CLFLUSHOPT are recent additions for better pmem performance

## Slide 8: Challenge of Using Persistent Memory by Applications
Transaction atomicity
  Not allow the action of flushing persistent memory to be interrupted by other threads recall.
  Transaction are power fail safe: Intel platform builds the eight-bytes power-fail-atomic store by hardware, so for application developers, they MUST reference the interfaces defined in Persistent Memory Programming Model.
Managing Persistent Memory Space
  Support both byte addressable memory and block device models
Naming, Permission, and Isolation the usage of persistent memory by user-space applications
Notes: The fsync, msync and related system calls are still relevant for DAX. Instead of causing the kernel to write back dirty page cache pages to media, for DAX these system calls cause the kernel to flush modified data cache lines in the processor caches out to the NVDIMMs.
DAX requires support from the underlying filesystem. It is currently supported by XFS, ext4 and ext2.

## Slide 9: Persistent Memory – Architecture in Linux
Notes: DAX: File system extensions to bypass the page cache and block layer to mmap persistent memory, from a PMEM block device, directly into a process address space.
BTT: Block Translation Table: Persistent memory is byte addressable. Existing software may have an expectation that the power-fail-atomicity of writes is at least one sector, 512 bytes. The BTT is an indirection table with atomic update semantics to front a PMEM/BLK block device driver and present arbitrary atomic sector sizes.
LABEL: Metadata stored on a DIMM device that partitions and identifies (persistently names) storage between PMEM and BLK. It also partitions BLK storage to host BTTs with different parameters per BLK-partition. Note that traditional partition tables, GPT/MBR, are layered on top of a BLK or PMEM device.
Reference: https://nvdimm.wiki.kernel.org/

## Slide 10
http://www.uefi.org/sites/default/files/resources/ACPI_6.0.pdf
Notes: SPA: System Physical Address that can be accessed by CPU.
SPA Range Structure: Define memory mapped region address, length and properties.
SPA Range Structure GUID: describe the Address Range Type.
Memory Device to System Address Range Map Structure: memory device properties.
Interleave Structure: defines interleaving properties.
NVDIMM Control Region Structure: hardware identifiers, and block control window stuff.
NVDIMM Block Data Window Region Structure: block accesses.
Flush Hint Address Structure: flush pending operations.
DSM: Device Specific Method: ACPI method to to control specific device - in this case the firmware.
DCR: NVDIMM Control Region Structure defined in ACPI 6 Section 5.2.25.5. It defines a vendor-id, device-id, and interface format for a given DIMM.

## Slide 11: E820 Table Example
Notes: ACPI 6.0 formalizes e820-type-7 and efi-type-14 as persistent memory. Mark it "reserved" and allow it to be claimed by a persistent memory device driver.
https://lists.gnu.org/archive/html/qemu-devel/2017-07/msg09071.html

## Slide 12
http://www.uefi.org/sites/default/files/resources/ACPI_6.0.pdf
Notes: DSM: Device Specific Method: ACPI method to to control specific device - in this case the firmware.

## Slide 13: Example for DSM

## Slide 14: PMEM Namespace vs BLK Mode Namespace
Notes: NVDIMM_Namespace_Spec.pdf
An NVDIMM Namespace is the unit of persistent memory storage that appears in /dev as a device that you can use for I/O.
Region: A Region is a grouping of persistent memory storage that can be divided up into one or more Namespaces.
Namespace Type: Valid Types are PMEM and BLK
Namespace Modes include raw, sector, memory and dax
For both Legacy NVDIMMs and for PMEM Namespaces created using the memmap kernel parameter, the system defaults to a single PMEM Region and a single PMEM Namespace that takes up all the available space in the Region.
An Aperture, Control Register and Status Register group is collectively called a Block Window, hence the name of this Type of access as BLK.
BLK Namespaces do not have virtual addresses that correspond directly to the persistent memory media, BLK Namespaces do not support the DAX feature. Filesystems built upon BLK Namespaces use the page cache just like traditional storage.
The configuration for each NVDIMM is stored in the Labels held in the Label Space of that NVDIMM. These Labels help us keep track of which part of the NVDIMM is allocated for the PMEM Namespace and which parts of the NVDIMM are allocated to BLK Namespaces.

## Slide 15: LIBNVDIMM Kernel Device Model and LIBNDCTL Userspace API (1)
Three device drivers corresponding to enumerated NFIT namespaces’ definition
  nd_pmem: /dev/pmem  PMEM namespace defined persistent memory range
  nd_blk: /dev/nd_blk  BLK namespace defined memory-mapped-I/O apertures to access persistent storage
  nd_btt: /dev/btt  BTT namespace defined physical memory device in memory disk semantics (atomic sector update)
Support PMEM and BLK access modes on NVDIMMs via defining PMEM namespace, and BLK namespace
PMEM namespace behavior
  Access using load and store
  PMEM namespace is associated with an interleave Set in NFIT since the primary reason for a PMEM namespace is to be addressed as memory in the SPA (System Physical Address)
BLK namespace behavior
  Access using block operation
  Atomicity at block level: in case of power failure when writing, it can be rolled back/forward
  Indirect access through a BLOCK WINDOW: DSM example definition for BLK mode
    No mapping the entire memory
    Reduce address utilization
    Reduce risk of wrong addressed writes
Notes: CONFIG_BLK_DEV_RAM_DAX=y
CONFIG_FS_DAX=y
CONFIG_X86_PMEM_LEGACY=y
CONFIG_LIBNVDIMM=y
CONFIG_BLK_DEV_PMEM=m
CONFIG_ARCH_HAS_PMEM_API=y
BLOCK WINDOW : NVDIMM DSM Example Definition include Block Windows (BWs), which are apertures through which software can read and write block-sized chunks of NVM, which is to send I/O specifically to a single DIMM.
ACPI 6: http://www.uefi.org/sites/default/files/resources/ACPI_6.0.pdf
NVDIMM Namespace: http://pmem.io/documents/NVDIMM_Namespace_Spec.pdf
DSM Interface Example: http://pmem.io/documents/NVDIMM_DSM_Interface_Example.pdf
Driver Writer's Guide: http://pmem.io/documents/NVDIMM_Driver_Writers_Guide.pdf
Git Trees
LIBNVDIMM: https://git.kernel.org/cgit/linux/kernel/git/djbw/nvdimm.git
LIBNDCTL: https://github.com/pmem/ndctl.git
PMEM: https://github.com/01org/prd

## Slide 16: LIBNVDIMM Kernel Device Model and LIBNDCTL Userspace API (2)
Namespaces of PMEM and BLK defined in NFIT CANNOT be overlap
PMEM namespaces can span across multiple NVDIMMs (interleaving)
BLK mode namespaces can be in just one NVDIMM, there can be multiple BLK mode namespaces in one NVDIMM. For control purpose, there defined BLK Window namespace that convers BLK Control Window, and BLK Data Window.
PMEM Namespaces
Notes: ACPI 6: http://www.uefi.org/sites/default/files/resources/ACPI_6.0.pdf
NVDIMM Namespace: http://pmem.io/documents/NVDIMM_Namespace_Spec.pdf
DSM Interface Example: http://pmem.io/documents/NVDIMM_DSM_Interface_Example.pdf
Driver Writer's Guide: http://pmem.io/documents/NVDIMM_Driver_Writers_Guide.pdf
Git Trees
LIBNVDIMM: https://git.kernel.org/cgit/linux/kernel/git/djbw/nvdimm.git
LIBNDCTL: https://github.com/pmem/ndctl.git
PMEM: https://github.com/01org/prd

## Slide 17: LIBNVDIMM Kernel Device Model and LIBNDCTL Userspace API (3)
PMEM namespaces support interleaving
Notes: ACPI 6: http://www.uefi.org/sites/default/files/resources/ACPI_6.0.pdf
NVDIMM Namespace: http://pmem.io/documents/NVDIMM_Namespace_Spec.pdf
DSM Interface Example: http://pmem.io/documents/NVDIMM_DSM_Interface_Example.pdf
Driver Writer's Guide: http://pmem.io/documents/NVDIMM_Driver_Writers_Guide.pdf
Git Trees
LIBNVDIMM: https://git.kernel.org/cgit/linux/kernel/git/djbw/nvdimm.git
LIBNDCTL: https://github.com/pmem/ndctl.git
PMEM: https://github.com/01org/prd

## Slide 18: LIBNVDIMM Kernel Device Model and LIBNDCTL Userspace API (4)
BTT (Block Translation Table) namespace (Optional)
  Provides atomic sector I/O
  Optional layer on top of pmem or blk mode
  Atomicity at block level in block namespaces
  Block namespaces broken into arenas (up to 512GB)
    Arena info block (backup)
    Arena flog
    Arena map
    Arena data area
    Arena info block
Notes: NVDIMM Namespace: http://pmem.io/documents/NVDIMM_Namespace_Spec.pdf
BTT: Block Translation Table: A software mechanism for turning a byte-addressable Persistent Memory range into a block-organized range with powerfail write atomicity when a block is updated.
Powerfail Write Atomicity: A feature allowing writes (or stores to memory) of a certain size that cannot be torn by a system interruption like a power failure. After recovery, the area being written will contain either the old value or the new value, but not a mixture of the two.
https://github.com/pmem/pmdk/blob/master/src/libpmemblk/btt.c

## Slide 19: LIBNVDIMM Kernel Device Model and LIBNDCTL Userspace API (5)
LIBNVDIMM sysfs layout
  Control class device in /sys/class/nd/ndctlX : accept DSM messages to be passed to DIMM identified by its NFIT handle.
  Bus : sysfs “Bus” corresponding to NFIT configuration, 1:1 relation. /sys/devices/platform/nfit_XXXX.0/ndbusY
  DIMM: /sys/devices/platform/nfit_XXXX.0/ndbusY/nmemZ
  Region: /sys/devices/platform/nfit_XXXX.0/ndbusY/regionZ
LIBNDCTL APIs
  Context: ndctl_new(&ctx)
  DSM interface in sysfs: /sys/class/nd/ndctlX
  Bus Operation APIs:
    Registration: struct nvdimm_bus * nvdimm_bus_register(struct device * parent, structure nvdimm_bus_descriptor * nfit_desc)
    Enumeration: ndctl_bus_foreach(ctx, bus)
  DIMM APIs
    Create: struct nvdimm *nvdimm_create(struct nvdimm_bus *nvdimm_bus, ……)
    Enumeration: ndctl_dimm_foreach()
  Region: Registered for each PMEM range or BLK-aperture set, and the APIs respectively
    struct nd_region *nvdimm_pmem_region_create(struct nvdimm_bus *nvdimm_bus, ……)
    struct nd_region *nvdimm_blk_region_create(struct nvdimm_bus *nvdimm_bus, ……);
Notes: NVDIMM Namespace: http://pmem.io/documents/NVDIMM_Namespace_Spec.pdf
BTT: Block Translation Table: A software mechanism for turning a byte-addressable Persistent Memory range into a blockorganized range with powerfail write atomicity when a block is updated.
https://github.com/pmem/pmdk/blob/master/src/libpmemblk/btt.c

## Slide 20: LIBNVDIMM Kernel Device Model and LIBNDCTL Userspace API (6)
LIBNDCTL APIs
  Namespace: resolving DPA aliasing and LABEL specified boundaries in REGION, and populates one or more “namespace” devices. The arrival of “namespace” devices trigger either nd_blk or nd_pmem driver to be loaded and register a disk/block device. Namespaces are indexed relative to their parent region.
  For BLK namespace device, it has “sector_size” attribute;
  Sysfs node location: /sys/devices/platform/nfit_XXX.Y/ndbusZ/namespaceM.N
  Namespace APIs
    Namespace creation: Idle namespaces are automatically created by kernel if a given region has enough available capacity to create a new namespace.
      ndctl_namespace_set_alt_name(ndns, devname)
      ndctl_namespace_set_uuid(ndns, parameters->uuid)
      ndctl_namespace_set_size(ndns, parameters->size)
      ndctl_namespace_set_sector_size(ndns, parameters->lbasize) if BLK namespace
      ndctl_namespace_enable(ndns)
    Namespace enumeration: ndctl_namespace_foreach(region, ndns)
Notes: NVDIMM Namespace: http://pmem.io/documents/NVDIMM_Namespace_Spec.pdf
BTT: Block Translation Table: A software mechanism for turning a byte-addressable Persistent Memory range into a blockorganized range with powerfail write atomicity when a block is updated.
https://github.com/pmem/pmdk/blob/master/src/libpmemblk/btt.c

## Slide 21: LIBNVDIMM Kernel Device Model and LIBNDCTL Userspace API (7)
LIBNDCTL APIs
  Block Translation Table (BTT): block device driver that fronts either the whole block device or a partition of a block device emitted by either a PMEM or BLK namespace. Every region starts with at least one BTT (seed device) w/ attributes “namespace”, “uuid”, and “sector_size”, and then bind the BTT device to the nd_pmem or nd_blk driver depend on the region type.
  Sysfs node location: /sys/devices/platform/nfit_XXX.Y/ndbusZ/regionM/bttN
  BTT creation: An idle BTT device is created automatically per region, which is handled as “seed” btt device, and then assign it to consume PMEM or BLK namespace.
    ndctl_btt_foreach(region, btt)
    ndctl_btt_set_uuid(btt, parameters->uuid)
    ndctrl_btt_set_sector_size(btt, parameters->sector_size)
    ndctl_btt_set_namespace(btt, parameters->ndns)
    ndctrl_btt_enable(btt)
Notes: NVDIMM Namespace: http://pmem.io/documents/NVDIMM_Namespace_Spec.pdf
BTT: Block Translation Table: A software mechanism for turning a byte-addressable Persistent Memory range into a blockorganized range with powerfail write atomicity when a block is updated.
https://github.com/pmem/pmdk/blob/master/src/libpmemblk/btt.c

## Slide 22: Concepts of NVDIMM Device Model in Linux
Notes: Region: is the unnamed storage block in nvdimm, comparing against namespace.

## Slide 23: IXPDIMM – Intel NVDIMM TOOL
Notes: https://github.com/01org/ixpdimm_sw
https://github.com/01org/invm-frameworks

## Slide 24: Persistent Memory Development Kit
PMDK which allows applications to access persistent memory as memory-mapped files, as described in the SNIA NVM Programming Model.
PMDK is a project with the goal of making persistent memory programming easier. It currently supports ten libraries, targeted at various use cases for persistent memory, along with language support for C, C++, Java, and Python, tools like the pmemcheck plug-in for valgrind, and an increasing body of documentation, code examples, tutorials, and blog entries.
Source for PMDK: https://github.com/pmem/pmdk/

## Slide 25: Programming Models Supported in PMDK (1)
Notes: https://nvdimm.wiki.kernel.org/
https://github.com/pmem/pmdk

## Slide 26: Programming Models Supported in PMDK (2)

## Slide 27: Programming Models Supported in PMDK (3)

## Slide 28: Current State of Ecosystem

## Slide 29: SNIA (Storage Networking Industry Association) Standards
SNIA NVM Programming Model
  Describes the basic programming model used for accessing persistent memory, implemented in PMDK.
ACPI Spec
  Starting with version 6.0, defines the NVDIMM Firmware Interface Table (NFIT) which is how the existence of persistent memory is communicated to operating systems. The specification also describes how NVDIMMs are partitioned into namespaces, methods for communicating with NVDIMMs, etc.
UEFI Spec
  Covers other NVDIMM-related topics such as the Block Translation Table (BTT) which allows an NVDIMM to provide block device semantics.
NVDIMM Namespace Spec
  Described the namespace and BTT mechanisms.
NVDIMM Driver Writers Guide
  Adhere to the NFIT tables in the ACPI V6.0 specification, the Device Specific Method (DSM) specification and the NVDIMM Namespace Specification.
NVDIMM DSM Interface
  Targeted to writers of BIOS and OS drivers for NVDIMMs whose design adheres to the NFIT Tables in the ACPI specification. The document specifically discusses the NVDIMM Device Specific Method (_DSM) example.
Notes: https://nvdimm.wiki.kernel.org/

## Slide 30: Use Cases Supported by Persistent Memory
In-Memory Database: Journaling, reduced recovery time, Ex-large tables
Traditional Database: Log acceleration by write combining and caching, frequently updated metadata
Enterprice Storage: Tiering, caching, write buffering and meta data storage
Virtualization: High VM consolidation with great memory density
High-Performance Computing: Check point acceleration and/or elimination

## Slide 31: Questions
How to partition NVDIMM to support PMEM and BLK per concrete use cases, i.e. how much capacities for PMEM, and how much capacities for BLK?

## Slide 32: Reference
https://software.intel.com/en-us/persistent-memory
https://nvdimm.wiki.kernel.org/

## Slide 33: Backup

## Slide 34: PMDK Usage

## Slide 35: 6 Memory Order Model in C++ 11
Memory Order 值 | Memory Order 类型
memory_order_relaxed | Relaxed
memory_order_consume | Consume
memory_order_acquire | Acquire
memory_order_release | Release
memory_order_acq_rel | Acquire/Release
memory_order_seq_cst | Sequentially consistent